Oahu Railway and Land Company Locomotive # 60

Wheel arrangement –			2-8-2

Builder –				American Locomotive Company, Schenectady Works

Locomotive serial number –		66279

Year built –				March 1925

Gauge –					Three feet

Valve gear –				Walschaert

Valves –					Piston

Cylinders –				18 x 22 inches

Driving wheelbase –			12 feet 3 inches

Engine wheelbase –			28 feet 10inches

Overall length –				59 feet 8 inches

Overall width –				10 feet 6 inch

Overall height –				12 feet 6½ inches @ stack

Engine & tender wheelbase –		50 feet 11¾ inches

Weight in working order:

Drivers – 			119,000 lbs. (59.5 tons)

Total engine –			156,000 lbs. (78 tons)

Total engine & tender – 		239,300 lbs. (199.65 tons)

Tractive effort –				27,500 lbs.

Diameter of driving wheels – 		44 inches

Diameter of driver centers –		37 inches

Frame:

Top member –			4 to 4¾ inches by 4 inches

Bottom member –		3½ to 3¾ by 4 inches

Springs –				Standard driving leaf springs, 4 on each side

Cab –					Steel cab with seats, steam gauge, air gauge, three

gauge cocks and water glass. Cab wired for electric

illumination.

Air compressor –				Two single cylinder 9½ inch Westinghouse

Brakes –					Westinghouse automatic air brakes to all drivers,

tender wheels and for train. Brake valves, 2 -								Westinghouse H-6, S-6.

Diameter of boiler –			64 ¾ inch O.D., 63 ½ inch I.D., Type: Straight top

Allowed steam pressure –			200 psi.

Injectors –				2 Nathan Monitor #9

Lubricator –				One Nathan #31

Fire box length – 				70¼ inches

Fire box width –				56 inches

Turbo generator –			Pyle National Type E, 40 amp, 32 volts

Leading truck –				28 inches

Trailing truck –				30 inches

Tender –					Steel, “U” shaped

Water tank –				Steel, 3,000 gallons

Oil tank –			Steel, 1,800 gallons, mounted between legs of  “U” shaped

water tank

Wheel diameter –				26”

Trucks –					Arch bar w/elliptical and coil springs

Frame – 					10” channel

Set up in the company shops when new, # 60 was out of service in overhaul at her last inspection. Her fire box had been renewed and all boiler tubes replaced. #60 was reassembled following abandonment of the main line and could only be tested briefly on the piers. Costing $32,803.19 when new, #60 was offered for sale for $22,500. Although the other 2-8-2’s were scrapped in 1953, the OR&L decided to save #60 and she resided in the remains of the roundhouse at Iwilei until 1966 when she was sold for a scrap value of $700.00 and torched.